# BMC Configuration
Oct 2019

The BMC allows for remote management of the G8 server from a Web based UI. The advantages over using SSH are that you get access to things like the BIOS, the Console and can even start the server if it has done a power down.
Turn on the server from cold, and wait for the Boot Options page:
From this page select [F2] for the BIOS (you have to be quick, you only get about a second).
After a short time, you will see the initial BIOS page.
From this page, move down to and select Server Management.
When the Server Management page is displayed, you must scroll to the bottom of this page.
From the bottom of the Server Management BIOS page, select BMC LAN Configuration.
The BMC LAN Configuration page shows two sets of IP Settings. Baseboard LAN Configuration and Dedicated Management LAN Configuration.
It is the Dedicated Management LAN Configuration we need to set. If no BMC address has ever been configured, then it will be 0.0.0.0 for everything, you need to configure this for your network, in this example we have used the following:
IP Source - <Static> (you could use DHCP, but would still have to work out the assigned address)
IP Address - 10.43.30.21 - use your own IP settings
Subnet Mask - 255.255.255.0
Gateway IP - 10.43.30.254

Once the IP settings have been configured, you need to scroll to the top of the page, and select User Configuration.