# Enable Remote Access to GPIO Pins

If you are using your Raspberry Pi via SSH or a Remote Desktop session, you need to enable remote access of the GPIO Pins, to do this from the command line, do the following:
  sudo raspi-config
  ┌──────────────────┤ Raspberry Pi Software Configuration Tool (raspi-config) ├───────────────────┐
  │ │
  │ 1 Expand Filesystem Ensures that all of the SD card storage is │
  │ 2 Change User Password Change password for the default user (pi) │
  │ 3 Boot Options Choose whether to boot into a desktop envi │
  │ 4 Wait for Network at Boot Choose whether to wait for network connect │
  │ 5 Internationalisation Options Set up language and regional settings to m │
  │ 6 Enable Camera Enable this Pi to work with the Raspberry │
  │ 7 Add to Rastrack Add this Pi to the online Raspberry Pi Map │
  │ 8 Overclock Configure overclocking for your Pi │
  │ 9 Advanced Options Configure advanced settings │
  │ 0 About raspi-config Information about this configuration tool │
  │ │
  │ │
  │ <Select> <Finish> │
  │ │
  └────────────────────────────────────────────────────────────────────────────────────────────────┘
  Advanced Options:
  ┌──────────────────┤ Raspberry Pi Software Configuration Tool (raspi-config) ├───────────────────┐
  │ │
  │ A1 Overscan You may need to configure overscan if blac ↑ │
  │ A2 Hostname Set the visible name for this Pi on a netw ▮ │
  │ A3 Memory Split Change the amount of memory made available ▒ │
  │ A4 SSH Enable/Disable remote command line access ▒ │
  │ A5 SPI Enable/Disable automatic loading of SPI ke ▒ │
  │ A6 I2C Enable/Disable automatic loading of I2C ke ▒ │
  │ A7 Serial Enable/Disable shell and kernel messages o ▒ │
  │ A8 Audio Force audio out through HDMI or 3.5mm jack ▒ │
  │ A9 1-Wire Enable/Disable one-wire interface ▒ │
  │ AA GPIO Server Enable/Disable remote access to GPIO pins ↓ │
  │ │
  │ │
  │ <Select> <Back> │
  │ │
  └────────────────────────────────────────────────────────────────────────────────────────────────┘
  Select GPIO Server
        ┌──────────────────────────────────────────────────────────┐
        │ │
        │ Would you like the GPIO server to be accessible over the │
        │ network? │
        │ │
        │ │
        │ │
        │ │
        │ │
        │ │
        │ │
        │ │
        │ │
        │ │
        │ │
        │ │
        │ │
        │ <Yes> <No> │
        │ │
        └──────────────────────────────────────────────────────────┘
  You will get a confirmation that the GPIO Server is available.
  ┌──────────────────┤ Raspberry Pi Software Configuration Tool (raspi-config) ├───────────────────┐
  │ │
  │ 1 Expand Filesystem Ensures that all of the SD card storage is │
  │ 2 Change User Password Change password for the default user (pi) │
  │ 3 Boot Options Choose whether to boot into a desktop envi │
  │ 4 Wait for Network at Boot Choose whether to wait for network connect │
  │ 5 Internationalisation Options Set up language and regional settings to m │
  │ 6 Enable Camera Enable this Pi to work with the Raspberry │
  │ 7 Add to Rastrack Add this Pi to the online Raspberry Pi Map │
  │ 8 Overclock Configure overclocking for your Pi │
  │ 9 Advanced Options Configure advanced settings │
  │ 0 About raspi-config Information about this configuration tool │
  │ │
  │ │
  │ <Select> <Finish> │
  │ │
  └────────────────────────────────────────────────────────────────────────────────────────────────┘
  Now Select Finish - You will be back at the command prompt (you may need to reboot)