# Interface Config
Jan 2020

Introduction
When using the M1 chassis, it should have been installed using the official .ISO, so this is applicable to both RX1 and MKSP installation.
Even though the interface configuration may look okay, there is an issue with the way the interfaces are installed, to remedy this you can run a small script that will recreate all of the configuration files.
The script update_network_devices.sh can be downloaded here:
To use the script, copy it to a folder that you have rights to use (/mfeng/home) and give the file exectue rights:
  chmod +x update_network_devices.sh

Now run the file using the following command:
  ./update_network_devices.sh

The script will create new ifcfg-ethx files depending on installed hardware (what NIC cards you have installed).
Navigate to /etc/sysconfig/network-scripts and edit ifcfg-eth0 (as sudo)
  sudo /etc/sysconfig/network-scripts/ifcfg-eth0

Now add all of your IP Details.
Alternatively you can configure the interfaces via nmtui or the front panel (might have to reboot to use the front panel)
## Interface Script
#!/bin/sh
# Script to assign names and hardware IDs to ifcfg-net* files as well as turn on
# consistent NIC naming. This resolves the issue of NIC ports swapping around
# due to boot-time race conditions. It should be run manually once after upgrade
# if you have multiple NICs. However it will delete all network configuration
# and rename NICs to be net0, net1, etc, which is not supported by all software.
echo "RUNNING SCRIPT: update_network_devices VERSION 0.2"
# recognised NICs # from https://devicehunt.com/
DEVICE_CODE_ONBOARD="8086:1533" # Intel Corporation - I210 Gigabit Network Connection
DEVICE_CODE_10G_CARD="8086:10fb|8086:1572|8086:1528" # Intel Corporation - 82599ES 10-Gigabit SFI/SFP+ Network Connection
        # Intel Corporation - Ethernet Controller X710 for 10GbE SFP+
        # Intel Corporation - Ethernet Controller 10-Gigabit X540-AT2
DEVICE_CODE_1G_CARD="8086:1521" # Intel Corporation - I350 Gigabit Network Connection
TMP_FILE="/tmp/nic_order_tmp.txt"
FILE_ETHX_TEMPLATE=/etc/sysconfig/network-scripts/ifcfg-
GRUB_FILE="/etc/default/grub"
function create_ifcfg() {
touch $1
cat > $1 << "EOF"
TYPE=Ethernet
BOOTPROTO="dhcp"
ONBOOT=yes
PERSISTENT_DHCLIENT=yes
IPV6INIT=no
PEERNTP=no
EOF
chmod 755 $1
}
function detect_nic_card() {
    device_code=$1
    lspci_id=$(lspci -nn | egrep "\[${device_code}\]" | egrep -o "[0-9]{2}:[0-9]{2}\.[0-9]")
    for i in ${lspci_id};
    do
        mac_addr=$(dmesg | fgrep $i | egrep -o "(([0-9a-f]{2}:){5}[0-9a-f]{2})")
        echo "eth$net_index $mac_addr $i" >> $TMP_FILE
        net_index=$(( $net_index + 1 ))
    done
}
# Check we have root privledges
if [[ $EUID != 0 ]]; then
    echo "root privileges needed, please re-run with sudo"
    exit 1
fi
# Delete existing ifcfg files
mv ${FILE_ETHX_TEMPLATE}lo /tmp/ifcfg-lo
rm -Rf ${FILE_ETHX_TEMPLATE}*
mv /tmp/ifcfg-lo ${FILE_ETHX_TEMPLATE}lo
rm -rf $TMP_FILE
touch $TMP_FILE
# Create entries in nic order file
net_index=0
detect_nic_card $DEVICE_CODE_ONBOARD
detect_nic_card $DEVICE_CODE_10G_CARD
detect_nic_card $DEVICE_CODE_1G_CARD
#iterate through nic order file and update ifcfg files
echo "Hard coding ethernet devices as follows:"
while read line; do
    echo $line
    name=`echo "$line" | awk -F ' ' '{print $1}'`
    mac=`echo "$line" | awk -F ' ' '{print $2}'`
    ifcfg_file=${FILE_ETHX_TEMPLATE}$name
    # Check if an ifcfg file already exists for this interface and if not, create it
    if [ ! -f $ifcfg_file ]; then
        create_ifcfg ${ifcfg_file}
    fi
    # Remove entries that we are going to set from the ifcfg file
    sed -i '/DEVICE/d' ${FILE_ETHX_TEMPLATE}$name
    sed -i '/NAME/d' ${FILE_ETHX_TEMPLATE}$name
    sed -i '/HWADDR/d' ${FILE_ETHX_TEMPLATE}$name
    sed -i '/UUID/d' ${FILE_ETHX_TEMPLATE}$name #Remove UUID entry to ensure we do not have a conflict between current UUID and the MAC address
    sed -i '/NM_CONTROLLED/d' ${FILE_ETHX_TEMPLATE}$name
    sed -i '/^[[:space:]]*$/d' ${FILE_ETHX_TEMPLATE}$name # Remove blank lines
    # Add fields to ifcfg file
    echo "DEVICE=$name" >> ${FILE_ETHX_TEMPLATE}$name
    echo "NAME=$name" >> ${FILE_ETHX_TEMPLATE}$name
    echo "HWADDR=$mac" >> ${FILE_ETHX_TEMPLATE}$name
    echo "NM_CONTROLLED=yes" >> ${FILE_ETHX_TEMPLATE}$name
done <$TMP_FILE
# Finally, enable consistent naming which ensures ifcfg files are used
sed -i 's/net.ifnames=0/net.ifnames=1/g' $GRUB_FILE
grub2-mkconfig -o $(readlink -e /etc/grub2.cfg)
echo "Please review network configuration files ${FILE_ETHX_TEMPLATE}-X - THEN reboot"