# Check 1+1 SP Comms
Mar 2023

### Introduction

This is pertaining to an SP release in LB 5.0.9 (but not necessarily limited to this release) where there seems to be a bug with running Compact Mode and Content Extraction.
For some reason there is a process called ericsson-stream-processing-content-extraction that is being setup internally with a 'proxy'. The proxy is for comms between the service and whatever calls it in a containerised system, not in a RPM system. The proxy has to be removed, which thankfully is very simple.
To work out the status of the proxy setting we need to check the status of a service, however to get the latest status of the service we need to restart it, this can be done using the following:
  systemctl restart ericsson-stream-processing-content-extraction
There is no feedback from this command line.
To check the status of the service use the following:
  systemctl status ericsson-stream-processing-content-extraction
This will give an output similar to the following: