# MX8400 IP Configuration
The MX8400 IP Address can only be set from the Serial Port (if you don't know the current IP Address). During the life of the MX8400 the serial port speed has changed from 19200 to 115200 (8,N,!), Ensure you set the correct speed in the terminal software (recommend Putty).
To set the IP Address you have to login. Once you have a serial connection, use the following to login:
  Login
  Password:Purple

Now you can use the following commands:
Showip - Shows current IP Configuration
IPAddresses:
  Data Input Primary : 10.10.10.1, subnet 255.255.255.0, gateway 10.10.10.254
  Data Input Backup : 10.10.10.2, subnet 255.255.255.0, gateway 10.10.10.254
  Data Output Primary : 10.10.10.3, subnet 255.255.255.0, gateway 10.10.10.254
  Data Output Backup : 10.10.10.4, subnet 255.255.255.0, gateway 10.10.10.254
  Ctrl Primary : 192.168.31.8, metric = 5
  Ctrl Backup : 192.168.31.9, metric = 6
  Ctrl Virtual : 192.168.27.205
  Ctrl Subnet : 255.255.255.0
  Ctrl Gateway : 0.0.0.0
  CA Primary : 0.0.0.0, metric = 7
  CA Backup : 0.0.0.0, metric = 8
  CA Virtual : 0.0.0.0
  CA Subnet : 0.0.0.0
  CA Gateway : 0.0.0.0
  Time : 0.0.0.0 : 123
  ---------------------------------------
  Input Virtual IP Addresses
  Muxlet 1 : 0.0.0.0 Slot -1
  Muxlet 2 : 0.0.0.0 Slot -1
  Muxlet 3 : 0.0.0.0 Slot -1
  Muxlet 4 : 0.0.0.0 Slot -1
  Muxlet 5 : 0.0.0.0 Slot -1
  Muxlet 6 : 0.0.0.0 Slot -1
  Muxlet 7 : 0.0.0.0 Slot -1
  Muxlet 8 : 0.0.0.0 Slot -1
  ---------------------------------------
  Other Mux IP Addresses
  Muxlet 1 : 0.0.0.0 0.0.0.0
  Muxlet 2 : 0.0.0.0 0.0.0.0
  Muxlet 3 : 0.0.0.0 0.0.0.0
  Muxlet 4 : 0.0.0.0 0.0.0.0
  Muxlet 5 : 0.0.0.0 0.0.0.0
  Muxlet 6 : 0.0.0.0 0.0.0.0
  Muxlet 7 : 0.0.0.0 0.0.0.0
  Muxlet 8 : 0.0.0.0 0.0.0.0
setip ctrl v -i 2017 JAN 25 10:47:53: Uptime=0 days 02:35:14.584 NuTicks=0x8E2118 CPU=7%, HWM=7%
Command 'setip' : Set the IP address of a port. Usage:
       setip <port> (i[p] | m[ask] | g[ateway] | [m]e[tric]) (<ip address>|<metric:1..15)
        port = (ctrl | ca | di | do) (p | b | v)
setip ctrl v ip 192.168.27.205
Command 'setip' : Set the IP address of a port. Usage:
       setip <port> (i[p] | m[ask] | g[ateway] | [m]e[tric]) (<ip address>|<metric:1..15)
        port = (ctrl | ca | di | do) (p | b | v)
setip ctrl v i 192.168.27.205