# Failed Muse Install 1080p SDI Board

When 6.2 was released, we also had a new SDI Input board that supports 1080p. Unfortunately there is an issue with the SDI (deltacast) driver in the ISO that causes the Muse to reboot during the installation process, thus redering the server useless.
To fix this, follow this guide. This will be fixed by altering the ISO file, but this might be good information for the future, so I am writing this down.
### Recovery Overview

  1. Manually Install Deltacast Driver(s)
  2. Manually Remove Deltacast Driver(s) (this also removes rogue drivers that were in the ISO)
  3. Reinstall the whole package (including Deltacast Drivers)

yum install deltacast-x300-5.19-2.el6.x86_64.rpm
Loaded plugins: fastestmirror Setting up Install Process Examining deltacast-x300-5.19-2.el6.x86_64.rpm: deltacast-x300-5.19-2.el6.x86_64 Marking deltacast-x300-5.19-2.el6.x86_64.rpm to be installed Determining fastest mirrors Resolving Dependencies –> Running transaction check —> Package deltacast-x300.x86_64 0:5.19-2.el6 will be installed –> Finished Dependency Resolution
Dependencies Resolved
Package Arch Version Repository Size
Installing: deltacast-x300 x86_64 5.19-2.el6 /deltacast-x300-5.19-2.el6.x86_64 50 M
Transaction Summary
Install 1 Package(s)
Total size: 50 M Installed size: 50 M Is this ok [y/N]: y ←———————press y here Downloading Packages: Running rpm_check_debug Running Transaction Test Transaction Test Succeeded Running Transaction
Installing : deltacast-x300-5.19-2.el6.x86_64 1/1
server will reboot
yum -l installed
yum list installed
yum remove deltacast-x300.x86_64 Loaded plugins: fastestmirror Setting up Remove Process Resolving Dependencies There are unfinished transactions remaining. You might consider running yum-complete-transaction first to finish them. The program yum-complete-transaction is found in the yum-utils package. –> Running transaction check —> Package deltacast-x300.x86_64 0:5.19-2.el6 will be erased –> Finished Dependency Resolution
Dependencies Resolved
Package Arch Version Repository Size
Removing: deltacast-x300 x86_64 5.19-2.el6 installed 50 M
Transaction Summary
Remove 1 Package(s)
Installed size: 50 M Is this ok [y/N]: y Downloading Packages: Running rpm_check_debug Running Transaction Test Transaction Test Succeeded Running Transaction Warning: RPMDB altered outside of yum.
Erasing : deltacast-x300-5.19-2.el6.x86_64 1/1
Verifying : deltacast-x300-5.19-2.el6.x86_64 1/1
Removed:
deltacast-x300.x86_64 0:5.19-2.el6
Complete!
System rebooted
yum install -y *.rpm
Loaded plugins: fastestmirror Setting up Install Process Examining deltacast-hd-5.19-2.el6.x86_64.rpm: deltacast-hd-5.19-2.el6.x86_64 Marking deltacast-hd-5.19-2.el6.x86_64.rpm to be installed Loading mirror speeds from cached hostfile Examining deltacast-x300-5.19-2.el6.x86_64.rpm: deltacast-x300-5.19-2.el6.x86_64 Marking deltacast-x300-5.19-2.el6.x86_64.rpm to be installed Examining envivio-muse-6.02.00-081.x86_64.rpm: envivio-muse-6.02.00-081.x86_64 Marking envivio-muse-6.02.00-081.x86_64.rpm to be installed Examining ms416-2.0-15.el6.x86_64.rpm: 1:ms416-2.0-15.el6.x86_64 Marking ms416-2.0-15.el6.x86_64.rpm as an update to 1:ms416-2.0-9.el6.x86_64 Examining protobuf-2.3.0-8.el6.x86_64.rpm: protobuf-2.3.0-8.el6.x86_64 Marking protobuf-2.3.0-8.el6.x86_64.rpm to be installed Examining python27-2.7-5.r01.x86_64.rpm: python27-2.7-5.r01.x86_64 Marking python27-2.7-5.r01.x86_64.rpm to be installed Resolving Dependencies There are unfinished transactions remaining. You might consider running yum-complete-transaction first to finish them. The program yum-complete-transaction is found in the yum-utils package. –> Running transaction check —> Package deltacast-hd.x86_64 0:5.19-2.el6 will be installed —> Package deltacast-x300.x86_64 0:5.19-2.el6 will be installed —> Package envivio-muse.x86_64 0:6.02.00-081 will be installed —> Package ms416.x86_64 1:2.0-9.el6 will be updated —> Package ms416.x86_64 1:2.0-15.el6 will be an update —> Package protobuf.x86_64 0:2.3.0-8.el6 will be installed —> Package python27.x86_64 0:2.7-5.r01 will be installed –> Finished Dependency Resolution
Dependencies Resolved
Package Arch Version Repository Size
Installing: deltacast-hd x86_64 5.19-2.el6 /deltacast-hd-5.19-2.el6.x86_64 9.4 M deltacast-x300 x86_64 5.19-2.el6 /deltacast-x300-5.19-2.el6.x86_64 50 M envivio-muse x86_64 6.02.00-081 /envivio-muse-6.02.00-081.x86_64 377 M protobuf x86_64 2.3.0-8.el6 /protobuf-2.3.0-8.el6.x86_64 971 k python27 x86_64 2.7-5.r01 /python27-2.7-5.r01.x86_64 57 M Updating: ms416 x86_64 1:2.0-15.el6 /ms416-2.0-15.el6.x86_64 5.6 M
Transaction Summary
Install 5 Package(s) Upgrade 1 Package(s)
Total size: 499 M Is this ok [y/N]: y Downloading Packages: Running rpm_check_debug Running Transaction Test Transaction Test Succeeded Running Transaction
Updating : 1:ms416-2.0-15.el6.x86_64 1/7
Installing : protobuf-2.3.0-8.el6.x86_64 2/7
Installing : deltacast-x300-5.19-2.el6.x86_64 3/7
Installing : deltacast-hd-5.19-2.el6.x86_64 4/7
Installing : python27-2.7-5.r01.x86_64 5/7
Installing : envivio-muse-6.02.00-081.x86_64 6/7
configuring httpd … SUCCESS
Cleanup : 1:ms416-2.0-9.el6.x86_64 7/7
Verifying : envivio-muse-6.02.00-081.x86_64 1/7
Verifying : python27-2.7-5.r01.x86_64 2/7
Verifying : deltacast-hd-5.19-2.el6.x86_64 3/7
Verifying : deltacast-x300-5.19-2.el6.x86_64 4/7
Verifying : protobuf-2.3.0-8.el6.x86_64 5/7
Verifying : 1:ms416-2.0-15.el6.x86_64 6/7
Verifying : 1:ms416-2.0-9.el6.x86_64 7/7
Installed:
deltacast-hd.x86_64 0:5.19-2.el6 deltacast-x300.x86_64 0:5.19-2.el6 envivio-muse.x86_64 0:6.02.00-081
protobuf.x86_64 0:2.3.0-8.el6 python27.x86_64 0:2.7-5.r01
Updated:
ms416.x86_64 1:2.0-15.el6
Complete! [root@env-4e-960364 ~]#