# tcpdump more
Feb 2021

Here are some more great uses for tcpdump.
tcpdump -i eth0 -nn -Q in
Shows only the 'input' traffic on the specified interface
Can also use -Q out for just outgoing traffic

tcpdump -i eth0-nn igmp
Shows only IGMP traffic on the specified interface
Can be combined with -Q in/out
tcpdump -i eth0 -nn igmp -Q in