# GPIO Inputs - LED Control via a Button and Interrupt

The previous example of using a button to light an LED, everything worked fine, but our processor was at 100%, this needs fixing, so in this example instead of constantly polling and setting GPIO pins, we are using a interrupt where by we do nothing until a button is actually pressed.
Create a new file in the normal way ( you can download the python file here to save time)
  sudo nano LED-Button-i.py
  #import modules
  import RPi.GPIO as GPIO # This imports the GPIO library that allows the use of the GPIO pins,
  import time # This imports the time library (for delays among other things)
        # These libraries are built in to Raspbian.
  GPIO.setmode (GPIO.BOARD) # This sets the GPIO pin numbering. Our LED is connected to Pin 12,
        # so we can reference it by using BOARD as pin 12. However there is
        # another option (BCM) where we can reference a pin by it's name, pin
        # 12 is called GPIO18 (a reference to its place on the chip).
  GPIO.setup(11, GPIO.IN, pull_up_down=GPIO.PUD_DOWN) # setup GPIO Pin 11 as an input, and set
        # the resistor to Pull Down (PUD_DOWN)
        # this is the pin the button is connected to
        # button is connected from pin 11 to the
        # +3.3v pin on the GPIO
  # this def buttonPressed needs to be defined before it can be reference in the GPIO.add_event_detect
  def buttonPressed(channel): # this is where our code will look when button is pressed
      print "Button is Pressed" # print something to the screen
      GPIO.output(12,1) # set GPIO pin 12 to high (3.3v) so LED will come on
  # this is where we setup the GPIO input to use the event buttonPressed that was
  # defined previously. bouncetime is a simple switch debouncer in mS.
  GPIO.add_event_detect(11, GPIO.RISING, callback=buttonPressed, bouncetime=500)
  GPIO.setup(12, GPIO.OUT) # Sets the GPIO pin as output. This is connected to the LED, then
        # from the LED to 0v via a 330 Ohm resistor.
  GPIO.output(12, 0) # sets the GPIO Pin 12 to low (so 0v)
  try:
        while True: # start a loop
        time.sleep(1) # 1 second delay (or LED wont stay illuminated
        GPIO.output(12,0) # Set PIN 12 to 0v so LED is off
  except KeyboardInterrupt: # if Ctrl-C is pressed, exit loop
        GPIO.cleanup() # reset GPIO pins to default state
  #End

Once you have your file saved, you can run it by using:
  sudo python LED-Button-i.py

## Example Output

Here you can see the code running (video)
The main advantage using the interrupt is that my processor occupancy on the Pi Zero is now around 10% normal, and 14% when I press the button. That's much better than the previous constant 100%.